## Slide 1
F5 & Intel Demonstrating ODL Enabled NSH-Based Service Function Chaining in Gi-LAN
9/27/2016 1:45pm
Tarek Radi, Comms Service Provider Solution Technology Enabling Manager, Intel
Randall Cleveland, Director of Solution Architecture, F5 Networks
Kevin Smith, Director of Platform Solutions, Intel

## Slide 2
Problem Statement & F5 contributions to date
Demo Topology and Flow
Demo
Key Learnings & Call to action
Questions and Comments
Agenda

## Slide 3
  Demo ODL-provisioned Network Service Header (NSH) Service Function Chaining using F5 commercial VNFs
  Primary goal of use case is functional integration of all disparate components
  Using existing open source technologies and F5 VNFs
  Based on publicly available open source technology as of Q1 2016 (ODL Lithium SR1)
  Open Daylight Controller provisioning of Service Function Classifiers and Forwarders
  Show case this solution with VNFs typically in Gi-LAN (applicable to other use-cases as well)
Target Solution Outputs
  Upstream patches and fixes as required
  Share Key Learnings and Interoperability considerations
  For more information about NSH in Gi-LAN see https://networkbuilders.intel.com/docs/Intel_evaluation_of_SFC_for_Gi-LAN_use_case.pdf
Problem Statement

## Slide 4
F5 have S/W defined applications that work in a S/W Defined Data Center (SDDC)
F5 BIG-IP Virtual Edition has a portfolio of VNFs that can be used in Gi-LAN & Enterprise infrastructures
F5 Virtual Network Functions (VNFs)
Virtual CGNAT (vCGN)
Virtual Traffic Detection Function (vTDF)
Virtual Content Insertion (vCI)
Virtual TCP Optimization (vTCPO)
Virtual SIP Routing and Load Balancing (vSRLB)
Virtual Secure Web Gateway (vSWG)
Virtual Firewall (vFW)
Virtual URL Filtering (vURL Filtering)
Virtual Bandwidth Controller (vBWC)
Virtual Application Delivery Controller (vADC)
Virtual DNS (vDNS)
Virtual Web Application Firewall (vWAF)
Virtual Access Policy Manager (vAPM)
Note
in this demo, instead of using the F5 L4-L7 TDF, F5 implemented an nsh_classifier iRule in the vADC to create a simpler L3 classifier
For more information about the above, see https://www.f5.com/pdf/solution-center/network-functions-virtualization-nfv-solution-overview.pdf
Notes: F5 offers a broad portfolio of products and solutions that allow maximum flexibility as you deploy and virtualize your network. Whether you need to virtualize elements in your S/Gi network (such as policy management, Gi Firewall, CGNAT, or intelligent traffic steering), or virtualize your control plane (using DNS and Diameter signaling), F5 VNFs can help you achieve your goals.

## Slide 5
Demo Topology and Flow

## Slide 6
Gi-LAN
Evolved Packet Core
Service Function Demo Overview
During mobile session establishment, the PGW assigns IP address and binds bearer to the traffic policy. PGW APN definition provides IP Pool info, either provisioned locally on the PGW or retrieved from AAA during authentication/authorization. The PGW also retrieves additional policy rules for bearer from PCRF.
AAA
PCRF
APN
Default Bearer
For Demo Purposes, Service Function Classification is based on Source IP Address
Scenario #1: Default path SSH to WebServer. (no service function policy match)
Based on Source IP from APN1, no service function policy match in classifier, SSH request does not traverse any SF VNFs
Scenario #2: Secure Web traffic scenario. (SFC_A = Firewall)
Based on Source IP from APN2 IP Pool, SFC resolves to assign SFC_A: Using 1 SFs to secure delivery of HTTP and block SSH based traffic.
Scenario #3: Video/media delivery scenario. (SFC_B = Firewall, URL Filtering, BW Control)
Based on Source IP from APN3 IP Pool, SFC resolves to assign SFC_B. Using 3 SFs to secure, enrich and optimized the delivery of video
Web Server
APN 1
APN 3
APN 2
ODL
External Packet Data Network
Service Function
Classifier
Firewall
URL Filtering
Bandwidth Control
PGW
APN_1 IP Pool
APN_2 IP Pool
APN_3 IP Pool
RestfulAPI
Notes: Improving user experience and providing protection to the mobile network at the connectivity, network, and application levels.
Providing security to the network and context for downstream web applications
Notes for Randy: the F5 VNFs support L4-L7 only, hence NSH is important since it allows for stateful devices to exist in a service chain. This is also why F5 don’t have a lot of interaction with ODL

## Slide 7
S/W and H/W Stack
Controller (Server2)
Intel WildCat Pass S2600WTT
Intel® Xeon® E5-2699 v3 2.30GHz,
72 logical cores (Haswell)
2.3.90
1.2.17
2.2.1
CentOS 7.1 (kernel = 3.16.3-1.el7)
Lithium SR1
Compute (Server#1) hosting user VMs and WebServer
Intel WildCat Pass S2600WTT
Intel® Xeon® E5-2699 v3 2.30GHz,
72 logical cores (Haswell)
Compute (Server#3) Hosting F5 Classifier
Dell PowerEdge R730
Intel® Xeon® E5-2690 v3 2.60GHz,
48 logical cores (Haswell)
Compute (Server#4) Hosting F5 VNFs
Dell PowerEdge R730
Intel® Xeon® E5-2690 v3 2.60GHz,
48 logical cores (Haswell)
2.4.90
1.2.17
2.0.0
CentOS 7.1 (kernel = 3.16.3-1.el7)
Classifier (BIG-IP 12.1.0.0.1434 + HotFix HF1-ENG19
2.4.90
1.2.17
2.2.1
CentOS 7.1 (kernel = 3.16.3-1.el7)
2.0.0
1.2.8
2.0.0
CentOS 7.1 (kernel = 3.16.3-1.el7)
2.4.90 with NSH patch
Firewall (BIG-IP 12.1.0.0.1434 + HotFix HF1-ENG19
URL Filter (BIG-IP 12.1.0.0.1434 + HotFix HF1-ENG19
Bandwidth control (BIG-IP 12.1.0.0.1434 + HotFix HF1-ENG19
VM1 (Ubuntu 16.04.01)
VM2 (Ubuntu 16.04.01)
VM3 (Ubuntu 16.04.01)
WebServer (CentOS 6.6)
Infrastructure
VMs
VNFs
1.5.3-86.el7+1.8
1.5.3-105.el7+2.1
1.5.3-86.el7+1.8
1.5.3-105.el7+2.1
Niantic 10Gb NIC
Niantic 10Gb NIC
Niantic 10Gb NIC
Niantic 10Gb NIC

## Slide 8
Server 3
Server 2
Server 4
IF
IF
OvS bridge SW3
F5 Classifier
Mgt-IP 10.241.105.50
IF
10.241.105.11
10.241.105.50 (floating)
10.241.105.14
10.241.105.25 (floating)
10.241.105.35 (floating)
10.241.105.45 (floating)
IF
ODL
Lithium
IF
10.241.105.8
OvS-DPDK bridge SW4
( SFF )
F5 Firewall
Mgt-IP 10.241.105.25
F5 URL-Filter
Mgt-IP 10.241.105.35
F5 Bandwidth-control
Mgt-IP 10.241.105.45
VxLAN-GPE (172.16.50.5)
NSH
tap5
em1
VxLAN-GPE
(172.16.50.100)
enp3s0f0
em1
Server 1
OvS bridge SW1
VM1
Default traffic
172.16.40.101
VNC port 1
VM2
(Accessing Web Traffic)
172.16.40.102
VNC port 2
VM3
(Accessing Video Traffic)
172.16.40.103
VNC port 3
Webserver
172.16.60.101
VNC port 5
IF
IF
10.241.105.5
Tap 5
(VLAN tag 4093)
enp3s0f1
enp3s0f0
172.16.60.100
172.16.20.200
172.16.40.100
Virtual server pool
Defined with IP
172.16.60.200 with
1 Node (webserver)
1Gbps
1Gbps
tap6
(VLAN tag 4093)
tap4
(VLAN tag 4094)
tap3
(VLAN tag 4094)
tap1
(VLAN tag 4094)
tap2
(VLAN tag 4094)
em2
em3
Internal SWITCH
172.16.20.23
172.16.20.35
172.16.20.45
172.16.10.3
1Gbps
Public and Management Network
1Gbps
em2
IF
172.16.10.6
172.16.20.6
br-underlay:
172.16.20.5
Ubuntu 16.04.01 VMs
CentOS 6.6 VM
CentOS 7.1 Core Host
F5 VNF

## Slide 9: Service Function Nodes/Chains/Paths in this Demo
Service Nodes
Service Function Chains
Service Function Paths

## Slide 10
Server 3
Server 2
Server 4
IF
IF
OvS bridge SW3
F5 Classifier
Mgt-IP 10.241.105.50
IF
10.241.105.11
10.241.105.50 (floating)
10.241.105.14
10.241.105.25 (floating)
10.241.105.35 (floating)
10.241.105.45 (floating)
IF
ODL
Lithium
IF
10.241.105.8
OvS-DPDK bridge SW4
( SFF )
F5 Firewall
Mgt-IP 10.241.105.25
F5 URL-Filter
Mgt-IP 10.241.105.35
F5 Bandwidth-control
Mgt-IP 10.241.105.45
VxLAN-GPE (172.16.50.5)
NSH
tap5
em1
VxLAN-GPE
(172.16.50.100)
enp3s0f0
em1
Server 1
OvS bridge SW1
VM1
Default traffic
172.16.40.101
VNC port 1
VM2
(Accessing Web Traffic)
172.16.40.102
VNC port 2
VM3
(Accessing Video Traffic)
172.16.40.103
VNC port 3
Webserver
172.16.60.101
VNC port 5
IF
IF
10.241.105.5
Tap 5
(VLAN tag 4093)
enp3s0f1
enp3s0f0
172.16.60.100
172.16.20.200
br-underlay:
172.16.20.5
172.16.40.100
Virtual server pool
Defined with IP
172.16.60.200 with
1 Node (webserver)
1Gbps
1Gbps
tap6
(VLAN tag 4093)
tap4
(VLAN tag 4094)
tap3
(VLAN tag 4094)
tap1
(VLAN tag 4094)
tap2
(VLAN tag 4094)
em2
em3
Internal SWITCH
172.16.20.23
172.16.20.35
172.16.20.45
1Gbps
Public and Management Network
1Gbps
em2
IF
1
2
3
4
5
8
9
10
11
12
13
172.16.10.6
172.16.20.6
172.16.10.3
Ubuntu 16.04.01 VMs
CentOS 6.6 VM
CentOS 7.1 Core Host
F5 VNF
6
7
Flow for Path #43

## Slide 11
Step 0: Tour ODL & F5 VNFs, especially Classifier and its “client_dg”, and URL filter’s “URL_Block_List”
Step 1: Using VM#1. No Restrictions
  Web traffic (HTTP) to WebServer – no restrictions for HTTP, JPG, or MP4
  SSH root@webserver. SSH Allowed
  Using tcmpdump, show no traffic in any of F5 VNFs
Step 2: Using VM#2: SFC with Firewall only. Firewall blocks SSH but allows HTTP
  web traffic to WebServer – no restrictions for HTTP, JPG, or MP4
  Using tcpdump, show traffic only in Firewall
  SSH root@webserver. SSH Allowed
  Classifier->Security->NetworkFirewall->ActiveRules and reject SSH traffic
  SSH root@webserver. SSH not allowed. Firewall functional!
Step 3: Using VM#3: SFC with Firewall + URL Filtering + Bandwidth Control
  Access http://webserver/MyPics
  Using tcpdump, show traffic only in all 3 VNFs
  Access http://webserver/MyPics/Pic1.jpg . Blocked due to URL filtering. Filter functional!
  Show Bandwidth-Control->Acceleration->RateShaping->Statistics. Reset shaper
  Access http://webserver/Videos/movie3.mp4. Access allowed. Show shaper incrementing
  Load up same video using VM#2 and compare speed. VM#2 catches up and goes further, faster. Rate Shaping functional!
Demo Steps

## Slide 12
DEMO

## Slide 13
Key Learnings & Call to Action

## Slide 14
MTU = Maximum Transmission Unit
Summary of key Issues Resolved
# | F5 Issues | Resolution/Workaround
1 | F5 Cross-service interoperability issue identified with OVS-DPDK | F5 provided hotfix HF1-ENG19 for BIG-IP v12.1.
2 | F5 VNFs implementation of NSH required iRule to decrement index | F5 provided sfc-nsh-vnf iRule (outbound & inbound). By Design.
3 | F5 VNFs were not handling traffic returning from WebServer | F5 provided nsh_sfc_proxy iRule for reverse traffic
4 | PMTU in F5 resulted in packet drops for large TCP packets which caused fragmentation in VXLAN tunnel | Config MTU=1300 on the client VMs

## Slide 15
# | ODL Issues | Resolution/Workaround
5 | Java error after launching ODL indicating too many open files | Workaround =Ulimit –n 32768. Issue confirmed as no longer reproducible in Boron
6 | When DPDK-enabled OVS acts as SFF, it needs a manually-added flow to push traffic to VNFs | Workaround=create separate overlay & underlay bridges Permanent fix = an patch is under development to add the flow automatically. Target to hit Boron SR1
Summary of key Issues Resolved

## Slide 16
Summary of key Issues Resolved
Infrastructure Issues
# | Infrastructure Issues | Resolution/Workaround
7 | NSH header in OVS 2.4.90 was incompatible with latest IETF NSH draft https://tools.ietf.org/html/draft-ietf-sfc-nsh-10 | The IETF-Compatible NSH patch https://github.com/yyang13/ovs_nsh_patches will be upstreamed to mainline OVS after resolving external dependencies

## Slide 17
# | Area | Issue | Actions taken in this PoC
1 | OVS-DPDK | VLANs could not be enabled with NSH-aware OVS-DPDK | Used non-DPDK OVS on servers where VLANs were needed. This is no longer an issue in Boron. Try it out!
2 | OVS | OVS 2.4.90 does not support NSH and VxLAN-GPE | DPDK-enabled OVS supports NSH (with patch). Switched from OVS to OVS-DPDK on servers where VxLAN-GPE was needed.
3 | F5 VNFs | F5 not fully integrated with ODL | F5 provided REST-ful API + bash scripts to add/delete/list/reset the DGL. F5 is developing an ODL RESTCONF integration to support SFCs
4 | Infrastructure | OpenStack’s implementation of SFC does not integrate with ODL | OpenStack de-scoped from this solution and VNFs deployed manually via QEMU. Others options include use of Tacker or Juju as a VNF-Manager.
Summary of Known unresolved issues
in ODL Lithium SR1

## Slide 18
Top 5 takeaways
Intel is taking a solution oriented approach that spans across communities, with contributions to ODL, OVS, FD.io, OpenStack, etc.
NSH-based SFC works with commercial F5 VNFs and ODL
F5 is evaluating accelerating their commercial VNFs using DPDK
Intel plans to enable OpenStack and MANO integration (e.g. OPEN-O and OSM)
vGi-LAN is one of the network segments that benefit from NSH-based SFC
Patches applied in this setup, and will now be available to you!
Notes:     Describe topology and the 2 scenarios:
      Scenario #1: APN1: Based on Source IP pick SFC#1: Video/media delivery scenario. Using 3 SFs to secure, enrich and optimized the delivery of video to the subscriber client. Improving user experience and providing protection to the mobile network at the connectivity, network, and application levels.
      Scenario #2: APN2: Based on Source IP pick SFC#2: Web traffic scenario. Using 2 SFs to secure and enhance the delivery of HTTP based traffic. Providing security to the network and context for downstream web applications
    See Client (VM#3) accessing WebServer for HTTP traffic, but not going through any SFs (no SFC defined) i.e. direct route to WebServer after going through classifier (no SFF)
    Show the configurations of the 3 Service Function VNFs
      SF1 = AFM (Advanced Firewall Manager), for Firewall and DDos Protection
      SF2 = LTM#1 (Local Traffic Manager) header enrichment, inserting subscriber information into the header for determining service context
      SF3 = LTM#2. (Local Traffic Manager) bandwidth control
    Show the configurations of F5 Classifier (i.e. tour its settings)
    Show that the OVS-DPDK ovs rules are empty
    Go to ODL and configure new SFC with 3 nodes in the chain (i.e. SFC#1: AFM -> LTM#1 -> LTM#2).
      Create 3 Service Functions types
      Create 3 Service Functions
      Ensure proper Locator IPs and settings
      Update SFF to be aware of the 3 SFs
      Created Scenario#1 Service Function Chain
      Created a Path from that SFC
      Deploy the Path enabling symmetry and got the 2 Path IDs (forward and revers)
    Show OVS-DPDK SFF details
    Updated the iRule in the F5 Classifier to use the new Path ID and the new Reverse Path ID
    Run Scenario#1, where Client#1 is accessing the webserver for Video/Media Traffic
    See traffic now going through:
      Classifier
        Incoming packet from client. Classifier encaps this packet
        Outgoing packet to webserver. Classifier has decap’d this packet
      SFF
        from Classifier to SFF,
        from SFF to AFM,
        from AFM to SFF,
        from SFF to LTM#1,
        from LTM#1 to SFF,
        from SFF to LTM#2,
        from LTM#2 to SFF,
        from SFF to Classifer
        AFM (from SFF to AFM, and from AFM to SFF) ^
        LTM#1 (from SFF to LTM#1, and from LTM#1 to SFF) ^
        LTM#2 (from SFF to LTM#2, and from LTM#2 to SFF) ^
^Note: Broadcasts will appear in the TCPDump on first packet
< ------------------------- Time permitting ------------------------à
11. Run video traffic and show that it is NOT going through SFC#1
12. Go to ODL and add a new SFC for scenario #2 (Web traffic), that is comprised only of AFM (i.e. SFC#2 = AFM -> LTM#1)
13. Run web traffic scenario from Client #2.
14. See traffic now going through AFM only and not through LTM#1 or LTM#2
15. Rerun scenario where client is accessing HTTP content on the webserver
16. See traffic now going through AFM, LTM#1 and LTM#2

## Slide 19
Call to Action to the community
From Intel
Join us to accelerate NSH as well as VxLAN-GPE upstreaming to OVS
We encourage VNF vendors to enable their VNFs to be NSH-aware for easier integration into NSH-based SFC solutions
Provide feedback on similar Solution Implementations & PoCs
Review upcoming whitepaper and Solution Implementation doc (https://networkbuilders.intel.com/network-technologies/solution-blueprints)
From F5
Allow for user-defined Path IDs instead of auto numbering
Enable a more generic list of Service Function Types in ODL
F5 will update this setup with latest ODL Boron release and patched OVS
Notes:     Describe topology and the 2 scenarios:
      Scenario #1: APN1: Based on Source IP pick SFC#1: Video/media delivery scenario. Using 3 SFs to secure, enrich and optimized the delivery of video to the subscriber client. Improving user experience and providing protection to the mobile network at the connectivity, network, and application levels.
      Scenario #2: APN2: Based on Source IP pick SFC#2: Web traffic scenario. Using 2 SFs to secure and enhance the delivery of HTTP based traffic. Providing security to the network and context for downstream web applications
    See Client (VM#3) accessing WebServer for HTTP traffic, but not going through any SFs (no SFC defined) i.e. direct route to WebServer after going through classifier (no SFF)
    Show the configurations of the 3 Service Function VNFs
      SF1 = AFM (Advanced Firewall Manager), for Firewall and DDos Protection
      SF2 = LTM#1 (Local Traffic Manager) header enrichment, inserting subscriber information into the header for determining service context
      SF3 = LTM#2. (Local Traffic Manager) bandwidth control
    Show the configurations of F5 Classifier (i.e. tour its settings)
    Show that the OVS-DPDK ovs rules are empty
    Go to ODL and configure new SFC with 3 nodes in the chain (i.e. SFC#1: AFM -> LTM#1 -> LTM#2).
      Create 3 Service Functions types
      Create 3 Service Functions
      Ensure proper Locator IPs and settings
      Update SFF to be aware of the 3 SFs
      Created Scenario#1 Service Function Chain
      Created a Path from that SFC
      Deploy the Path enabling symmetry and got the 2 Path IDs (forward and revers)
    Show OVS-DPDK SFF details
    Updated the iRule in the F5 Classifier to use the new Path ID and the new Reverse Path ID
    Run Scenario#1, where Client#1 is accessing the webserver for Video/Media Traffic
    See traffic now going through:
      Classifier
        Incoming packet from client. Classifier encaps this packet
        Outgoing packet to webserver. Classifier has decap’d this packet
      SFF
        from Classifier to SFF,
        from SFF to AFM,
        from AFM to SFF,
        from SFF to LTM#1,
        from LTM#1 to SFF,
        from SFF to LTM#2,
        from LTM#2 to SFF,
        from SFF to Classifer
        AFM (from SFF to AFM, and from AFM to SFF) ^
        LTM#1 (from SFF to LTM#1, and from LTM#1 to SFF) ^
        LTM#2 (from SFF to LTM#2, and from LTM#2 to SFF) ^
^Note: Broadcasts will appear in the TCPDump on first packet
< ------------------------- Time permitting ------------------------à
11. Run video traffic and show that it is NOT going through SFC#1
12. Go to ODL and add a new SFC for scenario #2 (Web traffic), that is comprised only of AFM (i.e. SFC#2 = AFM -> LTM#1)
13. Run web traffic scenario from Client #2.
14. See traffic now going through AFM only and not through LTM#1 or LTM#2
15. Rerun scenario where client is accessing HTTP content on the webserver
16. See traffic now going through AFM, LTM#1 and LTM#2

## Slide 20
Sessions:
  Fix Openflow Multiwriter issues in OpenStack + OVSDB + SFC Integration by using Genius and flow programmer (Yi Yang)
Demos:
  ODL SFC Solution with Integrated MANO in NFV (Yi Yang)
  We will provide a live demo of this PoC at the booth
Other recommended sessions

## Slide 21
Questions/Comments?

## Slide 22
Backup

## Slide 23: Service Function Chaining Overview in NFV Systems
Server A
VNF1
VNF2
vSwitch
NIC
VNFn
Server B
VNF1
VNF2
VNFn
vSwitch
NIC
Server C
VNF1
VNF2
VNFn
vSwitch
NIC
Classification & NSH VxLAN-GPE Encapsulation
NSH VxLAN-GPE De-encapsulation
NSH Forwarding
L2/L3 Forwarding
L2/L3 Forwarding
NSH: Network Services Header
VNF: Virtual Network Function
Service Function Chain starts and ends with the classifier
Service Chain #1
Service Chain #2
VNF Orchestrator (e.g. OpenStack) +
SDN Controller (e.g. ODL)
Deployment, Chaining, Steering
Notes: vSwitches are becoming overloaded
  Difficult to handle high data bandwidth with predictable latency
  Complex features such as NSH tunneling and forwarding consume CPU cores

## Slide 24
NSH Structure
Abstracted ID for Service Chain SC TTL
Examples:
TCP port 80,21,23 = SPI 12
IMEI iPhone6= SPI 10
16 bytes of mandatory context headers. These pass information between network nodes, classifiers and service functions.
Metadata Type indicates what context is being
included

## Slide 25
Running “ovs-ofctl dump-flows SW4” on Server4
OVS-DPDK on Server4 has a table of OpenFlow rules for each of the Service Function Paths
Rules show the ingress and egress points given a particular Index